New compressible fluid method

Equation	Description
C = 348.37	Gas constant of air
D = P / T * C	Density is equal to pressure / (temperature * gas constant)
dV = dP / D	Velocity change is equal to pressure gradient / density
nF = dV * D	Net inflow = net velocity*density
dP = nF	Pressure change = net inflow